## Slide 1: Presentation of Findings
Group 4: Body

## Slide 2: Overview
Shape and Size : Douglas Raymond
Materials: Nick Kamarianakis
Frame: Jacob Hawley
Lock Mechanism: Neal Traynor
Interior: Will Rose

## Slide 3: “What is the ideal shape and size for an electric assist bicycle?”
[1]
[2]
[3]

## Slide 4: Doors
Spring loaded Gullwing doors
[4]

## Slide 5: Shape
Aerodynamic like a raindrop
Dealing with rear tire snow buildup
  Partially covered back wheel
  Completely covered back wheel could collect a lot of snow
[5]

## Slide 6: Dimensions
2.4m long by 0.85m wide by 1.20m high
Surface area: Front:(Pi x radius x slant height) + Back:(1.2x0.85)+ Sides:2 x(0.6x1.2) =1.75+1.02+1.44 <4.2 metre squared (-0.2metres squared per wheel)

## Slide 7: Appearance
Customizable
  Decals – Option of lower price
  Paint job options – Better appeal

## Slide 8: Materials
(1) Housings of Electrical Components
(2) Outer “Shell” of Vehicle
Engineering Principles:
Durability and Strength to Weight Ratio

## Slide 9: Electrical Housings
Glass Filled Polycarbonate
Table 1 : Compressive strengths of Polycarbonate
Plastics International (2013) Zelux (Glass Filled Polycarbonate) [Online] Available: http://www.plasticsintl.com/datasheets/Polycarbonate_40_GF.pdf
http://www.youtube.com/watch?v=7TDnPLHXbyI

## Slide 10: Outer Shell
Glass-Fiber Reinforced Polyester
[1] [2] [3]
[1] http://www.solarwebsite.nl/en/2007/08/proefrit-aerorider/
[2] http://www.velovision.com/showStory.php?storynum=607
[3] http://www.examiner.com/article/aerorider-the-ultimate-single-seat-hybrid
Total Weight: 16kg (4kg/m2)
Total Price: 60$ (15$/m2)

## Slide 11: Frame
Force Distribution
  Wheel Base
  Seat Placement
Centre of Mass
  Seat Height

## Slide 12: Wheel Base
Long165-180cm
Short83-114cm
Compact Long114-165cm
120cm

## Slide 13: Seat Placement
By the rear tire
  Flip backwards
  Less sturdy
By the front tires
  Flip forward
  Bumpy ride
70/30 closer to the front tires
84cm

## Slide 14: Seat Height
Even with the centre of tires
Good Visibility
Sturdy

## Slide 15: Locking and Security
3 Principles:
Simplicity
Durability
Effectiveness
Primary option
Secondary option

## Slide 16: Primary Option
Primary option is to incorporate the existing vehicle door lock into the door of the recumbent tricycle

## Slide 18: Secondary Option
Secondary option is to use a standard bike lock and attach it to either the frame or an exposed wheel

## Slide 19
http://www.youtube.com/watch?v=I5pA_8Ut_J4
http://www.youtube.com/watch?v=8NK8zcZJif8

## Slide 20: Ergonomics

## Slide 21: Comfort

## Slide 22: Adjustability

## Slide 23: Adjustability

## Slide 24: Thank you for your time
Questions?